## Slide 1
2017_ver 1.0

## Slide 2: Technical Module
Introduction
2017_ver 1.0
Notes: The technical module section of the toolbox is designed to give the Environmental Officer (EO) more in-depth information about specific environmental topics. This introduction discusses environmental considerations that should be brought into the planning process. It first explains the need to take legal considerations into account. It then describes environmental characteristics that need to be considered when planning recce for base camp consideration, Environmental Baseline Surveys (EBSs), base camp layout, etc. Some of these considerations can also be relevant to the Energy Manager (EnM).
The following slides also apply when planning specific environmental functions, such as
-solid waste management
-hazardous material and hazardous waste management
-water and wastewater management
-spill prevention and response planning
-cultural property protection
-natural resources protection
Each of these are addressed in separate briefings within the technical module. In addition, this 2017 version has a new module, specifically focused on energy considerations.
See the “references module” part of the toolbox for additional general references (note: these have not been updated since the writing of the original toolbox was completed in 2013. Users are encouraged to identify new reference materials of specific utility to their individual needs). Each subject-specific technical module also has a list of additional references there.

## Slide 3: Laws and Regulations
Contact the legal office to determine the applicability of international treaties and agreements, national laws, host nation laws, mission regulations (United Nations (UN), North Atlantic Treaty Organization (NATO), European Union (EU), Theater command, etc.)
Be prepared to implement the highest applicable environmental standard
2017_ver 1.0
Notes: As an EO, you must contact the legal office to determine applicable international treaties and agreements, national laws, host nation laws, or mission regulations that pertain to environmental issues, such as waste management.
Although most laws and regulations do not specifically detail waste management procedures, they do require responsible parties to properly manage their hazardous materials and wastes. For international treaties or protocols such as the Basel Convention, even if your country has not signed and ratified the agreement, the country you are in may have done so, and this could impact your mission. As another example, cultural property must be respected in accordance with the 1954 Hague Convention.
Usually the most stringent regulations apply, if feasible and practicable for the operation. EOs should keep in close communication with the legal office to provide the necessary guidance and to ensure an understanding of all applicable treaties, agreements, laws, regulations, and standards. Thus, while the EO has the responsibility for reaching out to the legal staff for information, it is the legal staff that has the responsibility for determining issues such as whose environmental legislation and regulations will prevail in given circumstances.

## Slide 4: Siting Considerations (1 of 2)
Early involvement in the base camp planning process is the best way to positively influence a mission’s environmental and energy considerations
Site operations to
  Maximize mission effectiveness
  Maintain accessibility
    If possible, ensure that proposed operations are accessible by an existing road network
  Maintain required standoff distances
    Standoff distances are especially important for force health protection reasons for areas such as: airfield operations, living quarters, base perimeter, wells, surface water sources, potential causes of contamination and sources of noise (e.g. generators)
    Cultural and archaeological properties and natural resources
  Minimize potential health impacts to base personnel and local population
2017_ver 1.0
Notes: These introductory slides to the technical module lay out issues that should be taken into consideration when setting up the base camp and determining what equipment to use. These are:
Siting considerations
Climate data
Topography
Hydrology
Soil characteristics
Cost-benefit analysis
This slide and the next list various siting considerations. First and foremost, the earlier an EO and EnM can have input into siting considerations, the more likely it is that environmental and energy factors will be addressed.
As noted throughout this toolbox, making sure the mission can be accomplished is paramount. Taking environmental and energy factors into account can actually help maximize mission effectiveness. In the case of “standoff distances,” for example, it is important to consider sufficient distance around airfield operations, munitions storage areas and living quarters. Similarly, potential sources of contamination should be located far away from wells. The proper siting of buildings can help reduce energy requirements.

## Slide 5: Siting Considerations (2 of 2)
  Minimize impact on the local environment
    Limit environmental degradation
    Properly manage and protect natural resources
    Preserve cultural property
  Maximize energy efficiency by taking into consideration natural light, sun intensity, wind direction, etc.
  Use existing roads and buildings, if possible
  Properly plan to allow for changes in mission and base population without having to construct additional solid waste and wastewater treatment sites, if at all possible
  Properly plan for training areas in or near the camp, which can involve building barriers, creating camouflage, and other activities that can impact the surrounding environment
2017_ver 1.0
Notes: Environmental protection considers not only effects on natural resources and ecosystems but also on quality of life. Quality of life considerations can include the impact of noise on base personnel and the local community.
To enhance energy efficiency, building design and siting should take into account factors such as the direction and intensity of the sun to make maximum use of natural light when feasible, shading in hot climates, and warming in cold climates.
A major challenge affecting siting is the likelihood that the mission might change, which could include increase or decrease the number of people deployed at the base. Being able to plan for some such fluctuations from the start can help minimize the need to build additional waste and wastewater treatment facilities later on.

## Slide 6: Climate Data
Temperature
  Temperature range and seasonal variability can affect equipment performance, energy requirements, and resource availability
Precipitation
  Precipitation, with seasonal variability, will affect many aspects of operations including: surface water availability, groundwater recharge rates, effectiveness of evaporation beds and lagoons, potential to conduct burning operations and potential to generate contaminated leachate from solid waste
  Precipitation data, combined with topographic data, will also help determine siting requirements and transportation routes
Prevailing wind direction
  Consideration of wind data helps to avoid blowing snow and smoke or other air contamination toward the camp and other inhabited areas
Net evaporation rates
  Use net evaporation rates to determine total size requirements for evaporation beds and lagoons
2017_ver 1.0
Notes: For climate data, sources of information could include your government’s agencies that deal with meteorology and geography as well as the intelligence staff within the command.

## Slide 7: Topography
Natural drainage
  Consider natural drainage and how this will impact the conveyance of storm water through and around the camp
Slope or elevation
  Ensure proper slope of sewer lines in order to optimize operation of the wastewater system
Geological hazards:
  Seismic zones – Avoid placing piping or anything that requires an impermeable liner (e.g., engineered landfill) in a seismic zone due to potential damage in the event of an earthquake
  Floodplains, mudslide-prone areas, avalanche-prone areas, and other local natural hazards – Avoid siting operations in areas susceptible to flooding and other natural hazards because they can cause significant disruptions and lead to environmental contamination
2017_ver 1.0
Notes: One source for information on attributes such as seismic zones, floodplains, and other geological hazards are your government’s geography agency or intelligence agencies. In addition, the Global Seismic Hazard Assessment Program, sponsored by the United Nations, assembled the first consistent, worldwide maps of the threat of earthquake shaking. The various maps can be accessed via http://www.seismo.ethz.ch/static/GSHAP/ and also via http://geology.about.com/od/seishazardmaps/ss/World-Seismic-Hazard-Maps.htm. Also at this website, there is a link for “earthquakes in your region,” at http://geology.about.com/od/eq_regional/Earthquakes_in_Your_Region.htm. More generally, the website geology.about.com offers an easily accessible source for such data.

## Slide 8: Hydrology
Water quality and quantity
  The quality of water will determine treatment requirements
  If sufficiently available, groundwater is often a preferred drinking water source
  The available quantity of water will determine the need for delivering potable water and/or reducing use of available resources and what impact its use will have on local community and ecosystem
Groundwater resources, depth and availability
  Engineered landfills or lagoons should not be constructed in areas with high water tables due to the high likelihood of groundwater contamination
Surface water
  Surface water is the most accessible water source, but is often the poorest quality
Protected watersheds or aquifer recharge zones, wetlands
  Engineered landfills or lagoons should not be constructed near these sites
  It is best to conduct solid waste and wastewater operations downstream and as far as possible from water sources
2017_ver 1.0
Notes: The engineering staff within the command should be one source of information for hydrological data.

## Slide 9: Soil Characteristics
Permeability
  Highly permeable or porous soil will allow for contaminants to travel more quickly through the soil, which can lead to groundwater contamination or a greater volume of contaminated soil when performing clean up actions
  Low permeability soil - such as hard pan, frozen ground and permafrost - should not be disturbed if possible
Bearing capacity (the capacity of soil to support the loads applied to the ground)
  Loads surpassing the soil’s bearing capacity can cause severe settling and failure of the soil
  Fine soils have a low bearing capacity
  Seasonable variability can affect the soil’s bearing capacity
2017_ver 1.0
Notes: As with hydrological data, the engineering staff within the command should be one source of information for soil characteristic information.

## Slide 10: Soil Percolation Rates
Time required for water level to drop 2.5cm in a test hole | Relative absorption rate | Type of soil
0-3 minutes | Rapid | Coarse sand and gravel
3-5 minutes | Medium | Fine sand or sandy loam
5-30 minutes | Slow | Clay, loam, or clay with sands
30-60 minutes | Semi-impervious | Dense clay
> 60 minutes | Impervious | Hardpan or rock
Note: the first two types of soil are suitable for subsurface disposal. They are not suitable for lagoons unless water retention is assisted by the installation of an impermeable liner at the lagoon bottom. |  | 
2017_ver 1.0
Notes: Before selecting a gray water system, the absorption capability of the soil at the site must be determined by performing a percolation test or by obtaining preexisting data that may be available through geospatial engineer teams. Percolation testing to determine surface drainage for evaporation beds and soakage pits and trenches is performed using the following steps:
 Step 1: Dig one or more holes 30 cm square by 30 cm deep.
 Step 2: Fill the test hole(s) with water and allow it to seep into the surrounding soil.
 Step 3: Refill the hole(s) to a depth of at least 15 cm while the bottom of the hole is still wet.
 Step 4: Measure the depth of the water and record the time it takes for all of it to be absorbed into the soil.
 Step 5: Calculate the time required for the water level to drop 2.5 cm.

## Slide 11: Cost-Benefit Analysis
When determining appropriate technologies or procedures it is important to take a holistic approach considering all aspects, such as:
  Mission requirements
  Resources (availability of time, manpower, space, equipment, materials and transportation)
  Lifecycle costs (purchase, maintenance, disposition)
  Sustainable resource use (energy and water requirements, waste generation)
  Minimize environmental and logistical impacts
  Cultural acceptance
    Base populace
    Host nation
2017_ver 1.0
Notes: It is important to consider a range of factors when deciding which technology, processes, or types of supplies to use. The mission requirements set the overall parameters for what should be considered, although as already noted, these requirements can change over time and it is useful to be able to plan for some changes from the outset.
Other factors include resource considerations: do you have the necessary manpower to set up and run the equipment? Are the materials available? Is there sufficient space? Calculations about the overall “cost” should take a lifecycle approach: not only how much do the supplies or equipment cost, but how much does it cost to maintain them and how much does it cost to dispose of them? Similarly, how sustainable is the approach? What are the natural resource requirements? How much waste does it generate? It is also important to consider how well received the approach will be, both by the deploying forces and by the host nation. A well-documented case on “cultural acceptability” is the use of bottled water: in recent years, it has been difficult to change the mindset of deployed forces that bottled water is the preferred and healthiest option. This is certainly not always the case, but the mindset has been very hard to overcome.