## Slide 1
2017_ver 1.0

## Slide 2: Technical Module
Solid Waste Management
2
2017_ver 1.0
Notes: This Waste Management brief is designed to help the Environmental Officer prepare and plan for handling and managing non-hazardous solid waste. Hazardous materials and hazardous waste are addressed in a separate technical module.
The main elements are: waste reduction, waste segregation, storage and handling. Reuse and recycling may also be possible under some conditions. Planning is a key issue in waste management.

## Slide 3: Objectives
Understand the importance of solid waste (SW) management
Be familiar with common SW management procedures
Assemble data to make an informed choice for a SW management system
Know the key steps in waste planning
Develop knowledge about the risks, regulations and preventive measures in the handling of waste
Prepare for the most common obstacles of waste handling and management in operations and training
Know your responsibilities regarding waste management!
3
2017_ver 1.0
Notes: These lesson objectives emphasize the key points of this briefing.

## Slide 4: Definitions
Solid Waste (SW): Any substance, material or object which the holder discards, intends to discard, or is required to discard
Hazardous Waste (HW): Waste that because of its chemical reactivity, toxic, explosive, radioactive, or other characteristics, causes danger or is likely to cause danger, to health or the environment
Recycling: The reprocessing in a production process of the waste materials for the original purpose or for other purposes, including organic recycling but excluding energy recovery
Reuse: The use of an item again for the same or different function
Waste Management (WM): The collection, transport, reuse, recycling and disposal of waste, considered as a whole, including the supervision of such activities
Waste Segregation: The separation of waste materials on the basis of potential options for reuse, recycling, treatment and disposal
4
2017_ver 1.0
Notes: Definitions may vary from nation to nation and from organization to organization; these definitions are the ones used in the context of this toolbox.
Common to all definitions of hazardous waste (HW) is that hazardous material (HM) and HW are dangerous to humans or/and to the environment.

## Slide 5: Significance and Benefits
Good solid waste management can:
Enhance mission accomplishment and contribute to force protection by minimizing:
  Exposure to waste-related health issues and animal threats
  Unnecessary environmental and wildlife damage
Promote good relations with the host nation (HN) and local communities
Reduce the logistical footprint of the operation (camp space, transportation, funding, etc.)
5
2017_ver 1.0
Notes: There are a number of reasons that it is important to properly handle solid waste. This slide highlights the benefits that a good solid waste management plan can offer.
  Examples of minimizing exposure to waste-related health issues include: properly siting, operating and maintaining waste disposal areas, segregating waste at the point of generation, etc. Unconfined organic waste can attract wildlife, presenting a danger to personnel. Minimizing unnecessary environmental damage can be accomplished by reusing and recycling waste when feasible, composting biodegradable waste (depending on the duration of the operation), using more efficient technologies when possible, e.g. incineration instead of open burning.
  In promoting good relations with the HN and local communities, any additional agreements related to waste management should be taken into account.
In short, while solid waste can pose considerable environmental challenges, having proper management plans in place—as outlined in the remainder of this technical module—can significantly reduce those challenges.

## Slide 6: Negative Consequences
Poor waste and material management can cause:
  Direct health problems through vermin, air pollution and contamination of drinking water
  Large transportation and labor requirements
  Increased waste management at closure
  Potential security concerns
  Increased costs due to future liabilities
  Spoiling of the local environment by littering
6
2017_ver 1.0
Notes: Poor waste and material management can cause health and environmental problems. If waste is not handled, stored and managed properly, it can attract vermin and pests within the camp area. This increases the risk of spreading diseases. Waste can harm the drinking water source for the camp or others. If groundwater becomes contaminated, the consequences can be prolonged.
A burn pit can be a temporary solution to handle waste, but it entails several obstacles. If improperly located, wind directions can cause smoke and air pollution that directly affects the camp and surrounding areas. It is important to make sure the personnel take safety precautions handling the burn pit.
Leakage from buried or piled waste can contaminate groundwater and other aquifers, if not properly engineered and managed.
Waste handling requires equipment, transportation and logistics. This is not only an issue of land use, storage equipment and storage capability, but also a question of force protection. Every transport coming in or going out of the camp is an increased safety risk. It also requires resources in the form of manpower, personnel and money.

## Slide 7: Elements of a Waste Hierarchy
Reduce
Recycle
Recover
Dispose
Most Favored Option
Least Favored Option
Reuse
7
Segregation is a central element of waste management
2017_ver 1.0
Notes: The waste hierarchy, as depicted on this slide, guides waste management towards the most environmentally suitable option. Waste avoidance is the first step. Then comes reuse (i.e., multiple use for the same purpose), followed by recycling and treatment. If none of these steps are possible, waste disposal (e.g., landfill) is the last option. The applicability of each of these steps can vary, depending on the length of the operation.
Here are some additional considerations for each of these steps.
Reduce (avoid the generation of waste): Provide only what is needed. Use only what is needed. Remove disposable items. Avoid unnecessary packaging. Reuse: provide locations for exchanging personal or ordinary equipment such as concertina wire, wood, books, CDs, furniture and electronic equipment instead of discarding it.
Recycle: Ideally, recycled materials can be used for new products or for energy production. Some waste can be sold if it is sorted properly; having less waste also then reduces contractor costs. However, the costs of transportation would also need to be considered.
Recover (Treatment): can be biological, chemical or mechanical. As an example of a biological treatment, food waste can be composted to decrease unpleasant handling and transportation, although this is generally infeasible during a short-term operation and the most likely solution is to haul the waste out at the end of the operation. Most notable is the ability to recover waste for future energy generation.
Waste disposal: choose the best methods and techniques for waste disposal taking into consideration Host Nation (HN)/contractor capabilities, geography, etc.
These efforts require planning and maintenance. The sooner waste management and planning is taken into consideration, the easier and more effective the handling of waste will be. Segregation is a central element of waste management. Waste must be sorted as much as possible.
Note: NATO STANAG 2510 Environmental Protection (EP), Ed. 3, AJEPP-5 Joint NATO Waste Management Requirements during NATO-Led Military Activities, 31 October 2012 contains an example of a waste management hierarchy for NATO operations. In addition, refer to Annex D of NATO Standardization Agreement (STANAG) 2582 Environmental Protection (EP), Ed. 1, Allied Joint Environmental Protection Publication (AJEPP)-2 Environmental Protection Best Practices and Standards for Military Camps in NATO-led Military Operations

## Slide 8: EO Responsibilities
Develop the Solid Waste Management Plan, using the 6-step Waste Management Process
Train personnel on SW management requirements
Coordinate with other appropriate personnel to ensure safe procedures and protocols
Monitor performance of SW management systems
  Segregation, storage, transportation, contractor activity as applicable, etc.
Follow up and report
Maintain documentation
8
2017_ver 1.0
Notes: The EO should research issues pertaining to SW management. The research may include the availability and expertise of local personnel or contractors, best storage and treatment areas, water and wind conditions, and other limitations imposed by the geography. In cold weather, the options most often available are to store waste in containers (or with the individual) and then either to pack out the waste or incinerate it. If you are an EO taking over from another EO or unit personnel, contact them for assistance and information.
If there are no established safety procedures in the operation, the EO should develop those procedures. It is important to comply with safety procedures and protocols for storage, use, handling and transport. The EO also needs to make sure that necessary safety equipment is available. For information on safety equipment, see the ”Spill Response” technical module.
Certain details about SW management must be documented, such as the type of waste, the amount of waste, how it has been handled, transported, disposed of, and by whom. Such documentation must be saved for a certain amount of time, which will likely vary by country, waste stream and maturity of the operation.

## Slide 9: WM Process Overview
9
2017_ver 1.0
Notes: This overview follows the standard ”plan, prepare, execute” process where you conduct assessments at each of the stages. The boxes list details within each step of the process.
The source for this image is the US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015.

## Slide 10: Waste Management Plan
In a waste management plan, all waste management aspects must be dealt with. The waste management plan must comprise at least the following aspects:
A list and map depicting waste generation activities/locations and waste collection points for each differing waste stream (residual and recyclable wastes), including relevant information (e.g., points of contact)
A list of the types of waste, including estimated quantities and disposal capacities
Necessary safety and health information applicable to specific wastes generated
A list of local authorities, local laws and regulations and approved local contractors
Separation of waste by different categories/into different fractions
Procedural instructions for safe handling and disposal
Assignment of responsibilities within the military sector
Special considerations due to abnormal or exceptional weather conditions
10
2017_ver 1.0
Notes: The aspects presented in this slide are in accordance with NATO’s AJEPP-5.
Waste management should be considered in all processes, such as camp construction, equipment purchases and exercise planning.

## Slide 11: Six-Step SW Management Process
Initial considerations
Six-step development process
Analyze the situation: e.g., security level, weather, location, duration, size, geology and economy
Develop preliminary waste estimates for: kitchen, workshop, petroleum oils and lubricants (POL) handling, incoming goods, number of personnel, etc.
Categorize waste requirements (time-scale): appropriate methods are based on mission duration
Evaluate SW management capabilities: Personnel and staff, HN and/or contractors’ abilities, equipment options, etc. This includes evaluating the level of awareness of responsible individuals
Generate solutions suitable for the mission: solutions must meet specific requirements and be in accordance with the waste hierarchy
Integrate waste management tasks into plans and orders
Continue to monitor
11
2017_ver 1.0
Notes: Waste management should not be pursued in an ad-hoc manner. For best results, SW management should be taken into consideration from the start and continuously updated thereafter. NATO AJEPP-5 prescribes different responsibilities for the Lead Nation (LN) and Sending Nation(s) (SN).
When planning SW management systems, you should include risk assessment to determine best practices and methods.
Methods and systems for SW management should be chosen based on several factors for the specific operation such as weather, geography; number of personnel and staff; security, health, and environmental considerations; and equipment options.
Evaluate SW management capabilities. What are the HN and/or contractors abilities for receiving and handling waste? What equipment do they have available? If the HN or local community is a party to waste management activities, a Memorandum of Agreement should be developed to clearly delineate responsibilities.

## Slide 12: Initial Considerations
Start planning early
  Fulfill current requirements and anticipate future needs
Conduct Environmental Baseline Study (EBS)
Site location
  SW storage should be downwind of living quarters
  Temporary storage areas should be sited as far as practicable from airfields to avoid bird strike hazards
  Allow easy access for collection vehicles
  Avoid sensitive cultural and environmental areas
Create SW segregation capabilities
Ensure waste storage areas are secured from animals
12
2017_ver 1.0

## Slide 13: Analyze the Situation
Considerations for planning
Mission
Local threat conditions, including presence of wild animals
Terrain and weather
Troops and support available
Time
Civil considerations
  Regulations
  Public relations
Available infrastructure
Others
13
2017_ver 1.0
Notes: In order to properly plan SW management, it is first important to determine how much SW is likely to be generated. This slide lists a number of factors that will affect both the amount of SW and the possible solutions. For example, time considerations can include not only the mission duration but also the amount of time available prior to deployment and time available to meet mission requirements.
Other considerations include:
Risks to groundwater, surface water, and sources of potable water; this includes evaluating the need for rain and melt-water control
Respiratory health hazards and hygiene risks
Noise and litter control
Fire safety
Vector and animal control
Gas generation and migration
Testing and disposal for ash if incineration is used
Dust control
Transportation and heavy equipment issues related to freezing and thawing soils
Some of these issues are addressed in more detail in the technical module’s “Introduction” briefing.

## Slide 14: Develop Preliminary Waste Estimates
Component | Rate (%)
Generation Rate on the Move – 1.8 kg / person / day | 
General refuse | 37.5
Food waste | 62.5
Total nonhazardous solid waste | 100%
Generation Rates in Base Camps – 4.5 kg / person / day | 
Plastic bottles | 4
Other plastics | 10
Aluminum | 1
Cardboard | 11
Paper | 20
Food waste | 12
Textiles | 2
Glass | 1
Scrap wood | 22
Miscellaneous | 17
Total solid waste | 100%
14
2017_ver 1.0
Notes: This chart is an example of waste characterization derived from the US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015. Every base camp may be different based on mission type and duration, personnel and national policies.
In cold weather, at a minimum it can be expected that there will be more food and plastic waste. This type of information is useful in planning for waste segregation requirements and reuse or recycling capability.

## Slide 15: Consider Duration of Mission
Short (sustained operations for a maximum of 60 days)
  Low-tech solutions and/or appropriate storage, carry out
Medium (Approximately 60-180 days)
  Portable technical solutions
Long (more than 180 days)
  (Semi-)permanent technical solutions
Closing
15
2017_ver 1.0
Notes: Expected mission duration will affect the choice of techniques and equipment used for waste minimization and SW management (recycling, recovery, treatment and disposal) options, as listed in the slides later in this presentation.
These modules focus on solutions and options as a follow-on to field expedient solutions required during initial deployment. The choice of methods are likely to become more complex as the base camp matures or the mission changes.

## Slide 16: Evaluate SW Management Capabilities
Can your unit meet its waste requirement needs?
Does your unit have adequate resources to include:
  Manpower
  Equipment
  Materials
  Funding
Evaluate staff capabilities and need for raising awareness
Identify potential shortfalls
  What are HN and/or contractor capabilities to address these shortfalls?
16
2017_ver 1.0
Notes: There are two ways to handle SW management responsibilities: within the unit or going outside the unit, relying on contractor or HN capabilities.
This slide first lists some of the factors to consider when determining if your unit will be able to meet SW management requirements. It then notes the option for seeking outside assistance to address potential shortfalls.

## Slide 17: Generate Solutions
Determine potential solutions that are:
  Feasible
  Suitable
  Sustainable
If contracting is required, ensure environmental considerations are included:
  Performance work statement
  Monitoring and evaluation plan
Evaluate options and present at Energy and Environmental Management Board (EEMB) for Commander’s decision on the approved course of action (COA)
17
2017_ver 1.0
Notes: The feasibility of solutions is based on the availability of:
manpower (and skill sets)
equipment
materials
funding
contracted support
cost-benefit analysis
The suitability of solutions is based on:
terrain characteristics, such as soil composition, surface configuration and slope
weather conditions, such as prevailing winds, humidity and precipitation
environmental conditions, including environmentally sensitive areas such as historical and cultural sites
health considerations in terms of health risk severity, probability of health risk and the ability to mitigate risk
cost effectiveness in terms of both initial and sustainment costs
The sustainability of solutions is based on:
mission demands
environmental considerations
acceptance or tolerance of the local population, host nation
allowable design and construction standards
cost effectiveness in terms of both initial and sustainment costs
In some cases, the deploying force will not be able to address all SW management requirements internally and will therefore have to rely on contractor support. It is important to incorporate environmental considerations into the contract specifications.
Once solutions have been identified and prioritized, the EO should present these for consideration by the EEMB and the commander.

## Slide 18: Integrate SW Management into Plans and Orders
Finalize the plan that supports the approved COA
The plan should contain the who, what and when for each step in the SW management process:
  Reduction (waste avoidance and minimization)
  Segregation/Collection
  Transportation
  Recycling/Reuse
  Treatment
  Disposal
18
2017_ver 1.0
Notes: SW management is the reduction (waste avoidance) and minimization, segregation/collection, transportation, recycling/reuse, treatment, or disposal of waste materials in an effort to ensure a healthy and sanitary environment for base personnel, while preserving the environment and sustaining mission readiness. It also includes the measures and activities necessary for minimizing waste generation.

## Slide 19: Reduction (Waste Avoidance and Minimization)
Re-package material to minimize waste (“smart pack”) and use only what is needed
Reuse materials when possible instead of discarding them
  Create a location for reusing materials such as furniture, books, etc.
In procurement processes, focus on ways to minimize waste and potential negative environmental impacts:
  Avoid products with unnecessary packaging or packaging that is difficult to recycle or dispose
  Replace disposable items with reusable ones when possible (e.g., plates, silverware, trays)
  Avoid chemicals with negative health and environmental impacts
  Choose easily recyclable materials
  Use available technology to pre-process waste for recycling, treatment or disposal
Educate base personnel on waste avoidance and minimization
19
2017_ver 1.0
Notes: The information on this slide provides examples of ways to avoid or minimize waste.
These decisions are not all within in EO’s responsibilities, but they are important guidelines to take into consideration.

## Slide 20: Segregation/Collection
Segregate SW at point of generation in clearly marked containers to:
  Conserve resources
  Reduce chance of mishaps
  Minimize personnel exposure and prevent animal access
  Maximize recycling capability
Determine frequency and number of collection points needed
Educate base personnel on segregation requirements
Color coded containers simplify segregation
20
2017_ver 1.0
Notes: The next step in waste management is to segregate waste at the point of generation. This slide lists several of the benefits segregation offers. It is important, depending on the waste stream, to determine how often the waste needs to be transported from collection areas and how many collection points are needed. For example, paper may be collected weekly while food or sanitary waste may need to be collected daily to minimize health and hygiene risks.
Be sure to educate base personnel on these requirements. Every person is responsible for segregating his/her waste, but management of waste collection will be arranged by logisitics personnel.

## Slide 21: Transportation
Use vehicles dedicated for trash removal, if possible
  Bed should be covered to prevent trash blow off
  Minimize routes through billeting
  Perform dust abatement as necessary
Ensure personnel are wearing appropriate personal protective equipment (PPE)
21
2017_ver 1.0
Notes: If vehicles used for trash removal are used for other purposes, they should be sanitized prior to the other use.
If transporting waste off base or if a contractor is collecting waste on base, consider force protection requirements to minimize the potential threat to base personnel and operations.

## Slide 22: Recycling and Reuse
22
2017_ver 1.0
Notes: The images on this slide show some creative and practical ways of recycling and reusing materials in contingency environments. Examples include creating furniture from waste pallets, placing plastic bottle recycling containers immediately outside of latrines, and creating drop boxes to collect different types of used batteries.

## Slide 23: Treatment
Treatment: A change in character or composition of waste, to reduce or eliminate potential hazard
  Chemical – e.g., pH neutralization of waste sludge
  Biological – e.g., composting
  Mechanical – e.g., baling, shredding, compacting
Treatment may be performed in conjunction with or as a disposal method in itself
23
2017_ver 1.0
Notes: There are three types of treatment: chemical, biological and mechanical, as described on this slide.

## Slide 24: Disposal
The least desirable SW management option is disposal
Common disposal methods are technologies based on burying or incineration
If contractor support is required, perform quality assurance inspections to ensure proper handling and disposal of SW
24
2017_ver 1.0
Notes: As described in the waste hierarchy, every effort should be made to avoid or minimize waste. If avoidance is not possible, recycling and reuse methods should be utilized. Finally, whether done by your own forces or contract personnel, disposal of the remaining solid waste should be done in the manner that has the least negative impact on the environment.
Technologies for disposal are listed in slides later in this presentation.

## Slide 25: Continue to Evaluate and Monitor the SW Management Program
A successful SW management program is able to adapt to changing mission requirements
Maintain tracking documentation to improve estimates on waste generation quantities for each waste stream
Strive for continual improvement by upgrading SW management process as resources become available
25
Reduce
Recycle
Recover
Dispose
Most Favored Option
Least Favored Option
Reuse
Segregation is a central element of waste management
2017_ver 1.0
Notes: Changes in the SW management plan may be required for a number of reasons, such as:
Changes in duration of operations
Changes in camp population
Changes in type of operations
Changes in terrain
Changes in weather
Available Host Nation infrastructure
Available funding
All of these considerations should be monitored to ensure the SW management program continues to meet the unit’s needs.
Keeping good records is important not only for documenting what has been done, but also for improving estimates on the types and quantities of waste generated.

## Slide 26: Recycling and Bulk Minimization Options
26
2017_ver 1.0
Notes: The technical systems presented here are examples of methods and technology for recycling or minimizing the volume of waste within the camp. The advantages and disadvantages identified on the slides give you an idea of whether the method or technology is appropriate for your mission.

## Slide 27: Waste Oil Recycling
Advantages
  Reduces transportation
  Reduces logistics
  Possible energy source
  Saves resources
Disadvantages
  Oil quality not guaranteed for reuse
  Spill risks
Limitations
  Amount of waste oil
  Effectiveness in cold temperatures?
Duration Suitability Index |  | 
Short | Medium | Long
27
2017_ver 1.0
Notes: Recycling of waste oil is a method for re-using oil which reduces the amount of hazardous waste. Besides being environmentally beneficial, it saves resources in the form of reduced logistics demands, fewer personnel and less money. The recycled oil can also be used for energy production and contributes to a sustainable and self-sufficient camp.
Possible disadvantages with the recycling of waste oil is that you must have properly trained personnel, it might increase the risk of spill, and the oil quality might not work in delicate technology. Thus, before using recycled oil in vehicles or other technical apparatus, it is important to obtain approval indicating that it is suitable for such use.
This method is appropriate for medium- or long-term missions, but is less suitable for missions of short duration.

## Slide 28: Antifreeze Recycling
Advantages
  Reduces waste
  Reduces transportation
  Reduces logistics
  Saves resources
Disadvantages
  Quality not guaranteed for reuse
  Spill risks
Limitations
  Amount of antifreeze
Duration Suitability Index |  | 
Short | Medium | Long
28
2017_ver 1.0
Notes: Recycling of anti-freeze is a method for re-using anti-freeze. Besides being environmentally beneficial, it reduces the amount of hazardous waste and therefore resources in the form of reduced logistics demands, fewer personnel and less money.
Possible disadvantages with recycling of anti-freeze is that you must have properly trained personnel, it might increase the risk of spill, and the quality of the recycled anti-freeze might not work in delicate technology.
The method is appropriate for medium- or long-term missions, but is less suitable for missions of short duration.

## Slide 29: Oil-Contaminated Soil Composting
Advantages
  Does not leave contaminated soil
  Useable end product
  Reduces logistics
Disadvantages
  Land requirement
  Skilled personnel (education/equipment)
  Time (varies depending on temperatures)
Limitations
  Available material for composting (manure)
Duration Suitability Index |  | 
Short | Medium | Long
29
2017_ver 1.0
Notes: Contaminated soil can be remediated. Composting of POL-contaminated soil means that this soil will not need to be transported out of the camp. The treated soil can also be re-used for other purposes, such as in landfills or construction.
Disadvantages with composting of POL-contaminated soil is that it requires fairly large amounts of land and time for the proper management of the compost. The amount of time necessary can vary depending on the temperatures at the site (composting takes longer in cold temperatures). It is also necessary to educate personnel on composting processes, have the necessary equipment available (excavator + dense surface and cover), and have the personnel able to devote the time to managing the compost.
Other waste streams available for composting can be vegetative kitchen waste, sewage sludge and saw dust or paper products.
The composting of oil-contaminated soil is appropriate for medium- or long-term missions, but is less suitable for missions of short duration.

## Slide 30: Latrine Compost
Advantages
  Minimizes waste
  Reduces transportation
Disadvantages
  Handling latrine contents
  Health risks
  Time
  Space requirements
Limitations
  Space
  Infrastructure
  Appropriate only for small number of forces
Duration Suitability Index |  | 
Short | Medium | Long
30
2017_ver 1.0
Notes: Latrine contents are an organic resource that can be converted to soil filled with nutrients. The end product can be used as a soil enhancer. Composting of latrine products minimizes the infrastructure to transport the human waste. In places where piping or portable toilets and their management are unpractical or undesired, latrine composting is a good option. There are also other solutions for local treatments, including incinerating toilets but such solutions normally require energy.
Disadvantages with composting of latrine products is the health risk of handling and spreading products originating from human waste. Space for the composting chamber can also be a limitation.
The composting of latrine contents is appropriate for medium- or long-term missions, but is less suitable for missions of short duration.

## Slide 31: Dehydration and Slime Removal of Kitchen and Food Wastes
Advantages
  Combustible end product
  Reduces risk of smell and vermin
  Hygienic
  Reduces handling
  Space efficient
Disadvantages
  Capital cost
Limitations
  Only for food/wet waste
Duration Suitability Index |  | 
Short | Medium | Long
31
2017_ver 1.0
Notes: A dehydration and slime removal machine separates liquids from food waste, which results in a compact, dry and easily handled end product, which is free from smell and other nuisances. It facilitates the handling of food waste and reduces the risk of attracting vermin such as bacteria, flies and rats. It is also space efficient and decreases transportation requirements.
The main disadvantage of this system is the capital investment cost.
The dehydration and slime removal method is appropriate for medium- or long-term missions, but is not suitable for missions of short duration.

## Slide 32: Baling
Advantages
  Reduces transportation
  Space efficient
Disadvantages
  Capital costs
  Education of personnel
  Maintenance
Limitations
  Contractors’ ability to handle and receive baled material
  Enough material to bale
Duration Suitability Index |  | 
Short | Medium | Long
32
2017_ver 1.0
Notes: Baling of waste material is very space efficient, especially if you have a larger camp with large amounts of paper/cardboard waste material.
It is important to confirm that there are contractors who have the ability to handle baled waste materials before investing in a baling machine.
Disadvantages with baling are: capital investment cost, fairly large space requirements, and resources for the proper management of the baling machine. It is necessary to educate personnel, have necessary equipment available, and have the personnel able to devote the time to managing the machine.
The baling method is appropriate for medium- or long-term missions, but is not suitable for missions of short duration.

## Slide 33: Shredding
Advantages
  Reduces transportation
  Space efficient
Disadvantages
  Capital costs
  Education of personnel
  Maintenance
Limitations
  Contractors’ ability to handle and receive shredded material in a safe and proper way
Duration Suitability Index |  | 
Short | Medium | Long
33
2017_ver 1.0
Notes: Shredding waste material is very space efficient, especially if you have a larger camp with large amounts of waste metal, steel and/or aluminum.
Make sure that you have contractors who have the ability to handle shredded waste materials before investing in a shredding machine. Shredded metal can result in harmful sharp objects.
Disadvantages with shredding are: capital investment cost and resources for the proper management of the shredding machine. It is necessary to educate personnel, have the necessary equipment available, and have the personnel able to devote the time to managing the shredder. In addition, if there is a cold weather event where materials to be shredded freeze solid, processing may be difficult.
The shredding method is appropriate for medium- or long-term missions, but is not suitable for missions of short duration.

## Slide 34: Disposal Options
34
2017_ver 1.0

## Slide 35: Bury in Place: Simple Landfill
Advantages
  Low initial cost
  Low air emissions
Disadvantages
  Environmentally undesirable
  Labor intensive
  Land requirement
Limitations
  Only viable for small forces, short duration
  Non-hostile environment
Duration Suitability Index |  | 
Short | Medium | Long
35
2017_ver 1.0
Notes: A simple landfill is a pit that is dug and filled to not more than 30 cm (1 foot) from the top, then covered, compacted and mounded with 30 cm (1 foot) of earth. This is not a preferred option, but in small and short-term operations, it might be necessary. And it is more acceptable for organic waste. Check with local authorities about its acceptability. Such landfills will contaminate the soil and potentially ground water. It is important to locate it far from other camp activities.
More details about this disposal option are outlined on the next slide.

## Slide 36: Simple Landfill
General Design Considerations | A pit is dug and filled to not more than 30 cm from the top, then covered, compacted and mounded with 30 cm of earth. Bury in place should only be used when units are on the move or are stationary in a position for less than 1 week, or when established landfills are unavailable.
Limitations | Force Protection, environmentally undesirable, land availability, base population, health concerns (vector-borne diseases)
Recordkeeping, Reporting | Location, contents of waste, dates of burial, pictures
Capital Costs | None
Operations & Maintenance (O&M) Requirements | For a larger simple landfill, earthmoving equipment and additional manpower will be necessary
Transfer/Closure Requirements | Place a rectangular sign on top of the site indicating the type of pit/trench, the date it was closed, and the unit designation if the situation allows. An 8-digit grid coordinate is recorded for each waste burial site and reported to higher headquarters.
References | US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013 US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015 MCRP 4-11B, February 2010 U.S. Air Force, Environmental Considerations for Overseas Contingency Operations, Air Force Handbook 10-222, Vol. 4
36
2017_ver 1.0

## Slide 37: Burn Pit
Advantages
  Low initial cost
  Low operating cost
Disadvantages
  Negative environmental impacts
  Air emissions
  Human health effects
  Labor intensive
  Land requirement
Limitations
  Not authorized in many locations
  Cannot handle all waste types
  Needs to be sited far from personnel and airfields
Duration Suitability Index |  | 
Short | Medium | Long
37
2017_ver 1.0
Notes: Burning waste material is a short-term solution for SW disposal with a low initial cost. It is important to locate a burn pit far from other camp activities and taking wind direction into account. You want to minimize the risk of having smoke from the burn pit coming in to the camp, airfields, surrounding society, etc.
Disadvantages with burn pits are that they require fairly large amounts of land and resources for their proper management. They are environmentally unacceptable, contaminating the soil and air, and potentially ground water. It is also necessary to educate personnel on the burning processes, have the necessary equipment available, and have the personnel able to devote the time to managing the pit.
An important limitation is that, by policy, some militaries and host nations do not authorize the use of burn pits. It is therefore important to first determine if their use is even allowed.
A burn pit is appropriate for short- and medium-term missions, but is not suitable for missions of long duration.

## Slide 38: Burn Pit
General Design Considerations | Locate downwind of inhabited areas Do not conduct burn operations during weather prohibitive conditions (e.g. during or after rain events, during inversions)
Limitations | Recommendation – burn pit usage is not to exceed one year after the establishment of a base camp. Cannot burn covered wastes (e.g., plastics, hazardous waste, medical waste, tires, treated wood)
Recordkeeping, Reporting | Location, contents of waste, dates of opening/closure, pictures, amount, air sampling
Capital Costs | Earthmoving equipment
O&M Requirements | Manpower
Transfer/Closure Requirements | Soil sampling, groundwater sampling (consideration) Bury any existing trash and ash, cap existing area Place a rectangular sign on top of the site indicating the type of burn operations, the date it was closed, and the unit designation if the situation allows. An 8-digit grid coordinate is recorded for each waste burial site and reported to higher headquarters
References | US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013 U.S. Air Force Instruction, Waste Management, AFI 32-7042, 2010 US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015 MCRP 4-11B, Feb. 2010 U.S. Air Force, Environmental Considerations for Overseas Contingency Operations, Air Force Handbook 10-222, Vol. 4 U.S. Department of Defense Instruction (DODI) 4715.19, Use of Open-Air Burn Pits in Contingency Operations
38
2017_ver 1.0

## Slide 39: Air Curtain and Mobile Incinerator
Duration Suitability Index |  | 
Short | Medium | Long
Advantages
  Effective
  Land required only for the equipment
  Low air emissions
  Environmentally acceptable
  Easier to set-up than larger incinerator
Disadvantages
  High capital cost
  Transportation/logistics requirements
  Skilled operators
  High operations and maintenance (O&M) costs, including fuel
  Generated ash is HW
Limitations
  Acquisition and delivery timeline
  Suitable only for smaller force
39
2017_ver 1.0
Notes: More details about this disposal option are outlined on the next slide.

## Slide 40: Air Curtain and Mobile Incinerator
General Design Considerations | Locate downwind of inhabited areas Do not conduct burn operations during weather prohibitive conditions (e.g., during or after rain events, during inversions).
Limitations | Force Protection, land availability, base population, health concerns (vector-borne diseases) Cannot burn covered wastes (e.g., plastics, hazardous waste, medical waste, tires, treated wood)
Recordkeeping, Reporting | Location, contents of waste, dates of opening/closure, pictures, amount, air sampling
Capital Costs | Incinerator, earthmoving equipment
O&M Requirements | Manpower, fuel use, ash removal. Treat ash as HW
Transfer/Closure Requirements | Soil sampling, groundwater sampling (consideration) Treat any ash residue as HW. Sanitize and repack equipment for return to home station. Place a rectangular sign on top of the site indicating the incinerator operations, the date it was closed, and the unit designation if the situation allows. An 8-digit grid coordinate is recorded for each waste burial site and reported to higher headquarters.
References | US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013
40
2017_ver 1.0

## Slide 41: Fixed Incineration
Advantages
  Effective
  Land required only for the equipment
  Low air emissions
  Environmentally acceptable
Disadvantages
  High capital cost
  Skilled operators
  High O&M costs
Limitations
  Acquisition and delivery timeline
Duration Suitability Index |  | 
Short | Medium | Long
41
2017_ver 1.0
Notes: More details about this disposal option are outlined on the next slide.

## Slide 42: Fixed Incineration
General Design Considerations | Need to burn at proper temperatures, develop strategy for handling waste ash, fuel requirements, waste volume, liquids content of waste, waste composition. Redundancy (i.e., back-up solution because it is still necessary to dispose of waste if an incinerator experiences periods of inoperability), space to operate, scalability of system
Limitations | Requires skilled personnel to build, operate and maintain. Cannot burn covered wastes (e.g., plastics, hazardous waste, medical waste, tires, treated wood)
Recordkeeping, Reporting | Location, contents of waste, dates of opening/closure, pictures, amount, air sampling
Capital Costs | Incinerator and supporting facilities and equipment
O&M Requirements | Skilled manpower to operate and maintain, removal and disposal of waste ash, fuel costs
Transfer/Closure Requirements | Treat any ash as HW. Decide whether to remove incinerator or leave in place and associated follow on actions. Place a rectangular sign on top of the site indicating the incinerator operations, the date it was closed, and the unit designation if the situation allows. An 8-digit grid coordinate is recorded for each waste burial site and reported to higher headquarters.
References | US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013 U.S. Air Force Instruction, Waste Management, AFI 32-7042, 2010 US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015 MCRP 4-11B, Feb. 2010 U.S. Air Force, Environmental Considerations for Overseas Contingency Operations, Air Force Handbook 10-222, Vol. 4
42
2017_ver 1.0

## Slide 43: Engineered Landfill
Advantages
  Can handle all non-hazardous waste types
  Low air emissions
  Environmentally acceptable
Disadvantages
  High capital cost
  Labor intensive
  Large space requirement
Limitations
  Not viable for small forces, short duration
  Siting distance from personnel and airfields
Duration Suitability Index |  | 
Short | Medium | Long
43
2017_ver 1.0
Notes: More details about this disposal option are outlined on the next slide.

## Slide 44: Engineered Landfill
General Design Considerations | Must have an impermeable liner to prevent groundwater and soil contamination. Must have leachate and may need gas collection systems. Must not be sited within 3,000m of airfields to prevent the threat of bird strikes. A 4:1 ratio of waste to cover material is required. Daily cover is required to reduce risk from vectors and pests.
Limitations | Force Protection, land availability and exclusion zones, base population, health concerns (vector-borne diseases)
Recordkeeping, Reporting | Location, contents of waste, dates of opening/closure, pictures, amount, soil sampling, groundwater sampling
Capital Costs | Impermeable liner, leachate and gas collection systems
O&M Requirements | Manpower to compact solid waste, provide daily cover and construct cells
Transfer/Closure Requirements | Three basic goals need to be achieved: 1) minimize the need for further maintenance at the site, 2) place the landfill in a condition that will minimize future environmental impacts, and 3) prepare the site for future use.
References | US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013 U.S. Air Force Instruction, Waste Management, AFI 32-7042, 2010 US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015 MCRP 4-11B, Feb. 2010 U.S. Air Force, Environmental Considerations for Overseas Contingency Operations, Air Force Handbook 10-222, Vol. 4 U.S. Army, Sanitary Landfill, Technical Manual (TM) 5-814-5, January 1994 U.S. Corps of Engineers, Department of the Army, Engineering and Design: Sanitary Landfill Mobilization Construction, Engineering Manual (EM) 1110-3-177, April 1984
44
2017_ver 1.0

## Slide 45: Composting
Advantages
  Useable end product
  Reduces disposal requirements
  Environmentally acceptable
Disadvantages
  Capital cost
  Requires knowledgeable personnel
Limitations
  Only for biodegradable portion (food waste)
  Temperature limitations
Duration Suitability Index |  | 
Short | Medium | Long
45
2017_ver 1.0
Notes: More details about this disposal option are outlined on the next slide.

## Slide 46: Composting
General Design Considerations | Ensure a proper ratio of materials (Carbon:Nitrogen), wet and turn when required.
Limitations | Land availability, time requirement, cannot handle all wastes, temperature dependence
Recordkeeping, Reporting | Location, dates of opening/closure
Capital Costs | Composting containers and associated equipment
O&M Requirements | Manpower needed to monitor operations, wet and turn as needed
Transfer/Closure Requirements | If containers are used, determine whether to remove or leave in place
References | US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013 US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015 MCRP 4-11B, Feb. 2010 U.S. Air Force, Environmental Considerations for Overseas Contingency Operations, Air Force Handbook 10-222, Vol. 4 U.S. Corps of Engineers, Department of the Army, Composting for Army Installations, Public Works Technical Bulletin (PWTB) 420-49-14, 15 August 2000
46
2017_ver 1.0

## Slide 47: Host Nation Collection
Advantages
  No land requirement
  No capital investment
  Environmentally acceptable
Disadvantages
  Force protection
  Lead time for contract procurement
Limitations
  Limited by host nation’s capability
  Quality assurance inspection required
  Not suitable for sensitive material
Duration Suitability Index |  | 
Short | Medium | Long
47
2017_ver 1.0
Notes: More details about this disposal option are outlined on the next slide.

## Slide 48: Host Nation Collection
General Design Considerations | To protect base populace, locate solid waste transfer stations in a secure area with a route that does not pass by inhabited areas. Ideally, place the transfer station near or outside the base perimeter.
Limitations | Force Protection; lack of direct management oversight
Recordkeeping, Reporting | Copy of performance work statement and contract to provide proper quality assurance; contracting monitoring records
Capital Costs | Construction of a solid waste transfer station, waste transportation vehicles
O&M Requirements | Contract management
Transfer/Closure Requirements | Close contract and ensure contractor has fulfilled all requirements and received all required payments; sanitize and close transfer station; sanitize and prepare vehicles for final disposition
References | US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013 US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015. MCRP 4-11B, Feb. 2010 U.S. Air Force, Environmental Considerations for Overseas Contingency Operations, Air Force Handbook 10-222, Vol. 4
48
2017_ver 1.0

## Slide 49: Medical/Healthcare Waste Incineration
Advantages
  Effective
  Small land requirement
  Low air emissions
  Environmentally acceptable
Disadvantages
  Energy intensive
  Requires skilled operator
Limitations
  Acquisition and delivery timeline
Duration Suitability Index |  | 
Short | Medium | Long
49
2017_ver 1.0
Notes: More details about this disposal option are outlined on the next slide.
Note that NATO refers to “medical waste” as “healthcare waste.” NATO’s guidance on how such waste should be handled is contained in Annex C of NATO Standardization Agreement (STANAG) 2581 Environmental Protection (EP), Ed. 1, Allied Joint Environmental Protection Publication (AJEPP)-1 Environmental Protection Standards and Norms for Military Compounds in NATO Operations, 7 September 2011.
See also US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013, chapter 6 on medical waste.

## Slide 50: Medical Waste Incineration
General Design Considerations | Need to burn at proper temperatures, develop strategy for handling waste ash, fuel requirements, waste volume, liquids content of waste, waste composition Redundancy (need to dispose of waste should an incinerator experience periods of inoperability), space to operate, scalability of system. Remaining ash needs to be tested to determine if it is hazardous and must be disposed of properly.
Limitations | Requires skilled personnel to build, operate and maintain.
Recordkeeping, Reporting | Location, contents of waste, dates of opening/closure, pictures, amount, air sampling
Capital Costs | Incinerator
O&M Requirements | Skilled manpower to operate and maintain, removal and disposal of waste ash, fuel costs
Transfer/Closure Requirements | Decide whether to remove incinerator or leave in place. Dispose of any remaining ash Place a rectangular sign on top of the site indicating the incinerator operations, the date it was closed, and the unit designation if the situation allows. An 8-digit grid coordinate is recorded for each waste burial site and reported to higher headquarters.
References | US Army Technical Manual (TM) 3-34.56, Waste Management for Deployed Forces, 19 July 2013 U.S. Air Force Instruction, Waste Management, AFI 32-7042, 2010 US Army Techniques Publication (ATP) 3-34.5, Environmental Considerations, 10 August 2015 MCRP 4-11B, Feb. 2010 U.S. Air Force, Environmental Considerations for Overseas Contingency Operations, Air Force Handbook 10-222, Vol. 4
50
2017_ver 1.0

## Slide 51: Conclusion
Early SW management planning has many benefits. It:
  Enhances mission accomplishment by improving base camp quality of life
  Contributes to force protection
  Minimizes exposure to waste-related health issues
  Promotes good relations with the Host Nation and local community
  Reduces the logistical footprint of the operation (camp space, transportation, funds, etc.)
  Minimizes unnecessary environmental damage
Using a waste hierarchy helps to choose the best technology to minimize waste generation and save resources (manpower, funding and equipment)
Proper SW management minimizes closure requirements and possible environmental liabilities
51
2017_ver 1.0