## Slide 1
2017_ver 1.0

## Slide 2: Technical Module
Energy Considerations
2017_ver 1.0

## Slide 3: Objectives
Understand the importance of energy in the planning and execution of military operations and training
Raise awareness for all personnel about the impact that energy has on the mission and how behavioral changes can reduce energy requirements
Be familiar with planning considerations for the energy management components
Provide practical guidance for improving energy efficiency
2017_ver 1.0
Notes: These lesson objectives emphasize the key points of this briefing.

## Slide 4: Overview
Discuss objectives and definitions of energy considerations
Describe the significance of energy in operations
Identify planning considerations for optimal energy management
Provide examples of energy use in specific military operations
Present options for energy production, storage and distribution
Discuss energy efficiency practices
2017_ver 1.0
Notes: The presentation is organized into the sections identified on this slide.

## Slide 5: Definitions
Operational energy: the energy required for training, moving and sustaining military forces and weapons platforms for military operations
Energy efficiency: Using less energy to provide the same service
Renewable energy: energy generated from natural resources such as sunlight, wind, rain, tides and geothermal heat
Energy management: a balanced combination of energy awareness, behavioral practices and technology to systematically achieve energy efficiency for optimal military operations.
2017_ver 1.0
Notes: Source for definition of operational energy is from the 2016 US Department of Defense Operational Energy Strategy, page 3.
  Source of definition of energy efficiency: Lawrence Berkeley National Laboratory, which also notes that it is not the same as energy conservation. A similar definition by the International Energy Agency is ”a way of managing and restraining the growth in energy consumption.”
The definition for renewable energy is derived from the PennState Extension definition.
Energy management is a balanced combination of energy awareness, behavioral practices and technology to achieve energy efficiency for optimal military operations. (unknown source)
Energy management includes planning and operation of energy production and energy consumption units. Objectives are resource conservation, climate protection and cost savings, while the users have permanent access to the energy they need. It is connected closely to environmental management, production management, logistics and other established business functions. Source – Wikipedia.

## Slide 6: Responsibilities
All personnel have the responsibility to be good stewards of energy. They should be aware of their energy use and modify their behavior to reduce their energy consumption
The operational planner and camp planner have the primary responsibility for energy management and should coordinate with the safety, logistics and engineer staff
The commander is responsible for designating a specific energy manager, likely within the engineer staff, and authorizing him to coordinate with all other staff as necessary
The environmental officer is responsible for assisting the energy manager in identifying environmental impacts from energy practices and technologies and potential mitigation of those impacts
2017_ver 1.0
Notes: Although all personnel have responsibilities for efficient use of energy resources, the greatest impact can come in the initial planning stages when decisions regarding camp layout and energy usage are being made.
In contrast to the rest of the toolbox, energy management is not specifically an Environmental Officer’s responsibility. However it is still important for the EO to play a role in the Energy Management Program regarding potential impacts to the environment.

## Slide 7: Energy Facts
Two thirds of the fuel that a conventional diesel generator burns is blown out as heat. Only one third is converted into electricity.
In a typical military camp, 60-70% of fuel is used to produce electricity to heat/cool water or air.
Advanced technology and higher standards of living in camps have led to increased energy demand.
Depending on what role a soldier has, he may carry multiple types of batteries with at total weight of 4-12 kg (plus reserves).
Examples from Afghanistan:
      For each gallon of fuel, up to 4 gallons were consumed for transport.
      Fully burdened cost of fuel can be over 90€ per liter.
      On average there has been one casualty for every 24 fuel resupply convoys.
2017_ver 1.0
Notes: Source for battery data: ArmyTechnology.com, 1 July 2014, citing Dr. Cynthia Lundgren from the US Army Research Laboratory.
Source for examples from Afghanistan: http://www.natolibguides.info/smartenergy

## Slide 8: Benefits of Good Energy Management
Increases operational effectiveness and mission accomplishment
Reduces life cycle costs
Reduces logistical footprint (“More tooth, less tail”)
  Optimizes resource use (time, manpower, money)
Enhances force protection
  Saves lives
  Reduces the need for resupply convoys
Increases operational resilience
  Provides energy security
  Enables risk mitigation
Reduces negative environmental impact
Energy Demand
Operational Effectiveness
2017_ver 1.0
Notes: This slide describes why proper energy management is a mission enabler. It covers a number of benefits realized when energy demand is reduced.
When considering costs, it is important to consider the entire life cycle from procurement through disposition (for example maintenance, transportation and personnel requirements).
Image Source: Image courtesy of KROMKRATHOG at FreeDigitalPhotos.net

## Slide 9: Return on Investment for an Energy Efficient Camp
2017_ver 1.0
Notes: Behavioral changes and low-tech/low cost solutions will have a quick return on investment (ROI). This is an example of a calculation for a camp in Timor. As indicated in this example, the ROI for higher technology solutions is realized within 2 to 3 years.
So the anticipated duration of an operation will help to determine the optimal investment in energy-efficient systems and construction.
Source: Swedish FOI (Defense Research Agency) and United Nations Environmental Programme (2012): Greening the Blue Helmets

## Slide 10: Energy Planning
Energy Considerations
2017_ver 1.0

## Slide 11: Operational Energy Management Planning
Planning stage/pre-deployment: this is when the decisions are made that will determine how energy efficient the operation will be
Develop an energy management plan which includes:
    Energy use profile (baseline assessment of energy needs): where, how much, timing
    Energy production and distribution (energy budget/target, energy usage)
    Resources needed and possible alternative energy sources and configurations
    Responsible personnel
    Monitoring plan for energy use
Mission essential
Storage
Accomo-dation
Needs power 365/24/7
Can do up to 2 days without power
Can do longer without power
Planners should identify and prioritize which energy requirements are essential for the mission.
2017_ver 1.0
Notes: Mission accomplishment is a high priority when developing an energy management plan. Mission comes first!
The plan starts with a baseline assessment of energy needs: identifying who needs energy, when they need it, and what will impact energy usage (seasonal, time of day). After identifying needs, an energy budget determining production and distribution requirements must be created with associated targets for energy usage. Once the requirements are determined, the resources necessary to fulfill the production and distribution needs must be identified. It is at this point the opportunities to determine the feasibility of alternative energy sources and configurations should be analyzed. During this analysis, factors to be considered should include: security situation, local conditions (capacity, host nation support, feasibility of using renewable resources, etc.), mission duration and scale, and logistics footprint. The plan should also include integration of sensors and a routine monitoring process.
Further reading/references: NATO AJEPP 2 /STANAG 2582 Best EP Practices for Military Camps, Annex F.

## Slide 12: Duration of Operation
Photo credits: SwAF, and FOI
2017_ver 1.0
Short-Term | Medium-Term | Long-Term
Use natural lighting as much as possible Choose energy-efficient appliances where possible (e.g., fluorescent lights) Develop personnel awareness about energy saving | Establish micro grids for load balance and off peak power use (thus minimizing fuel needs) Plan and establish thermally insulated buildings only, where possible, with eco-efficient materiel (i.e., cellulose insulation) Plan and establish resource-saving installations Consider waste- to-energy conversion systems | Plan and establish alternative, renewable energy resources and waste-to-energy converters. Use newest techniques for efficient air-conditioning (i.e. heat-pumps). Establish a benefit system for successful energy/resources saving. Consider waste-to-energy conversion systems
Resources
Environmental
Requirements
Time
(Minimum Environmental Standards)
Developed
Base Camp
Bare Base
Notes: Energy issues are addressed in policy and doctrine documents such as:
Further reading/references:
NATO AJEPP 2 /STANAG 2582 Best EP Practices for Military Camps, Annex F.
European External Action Service (EEAS), European Union Military Concept on Environmental Protection and Energy Efficiency for EU-led Military Operations. EEAS: 14 September 2012.
UN DPKO/DFS, Environmental Policy for UN Field Missions (2009), para 37.
United Nations Environmental Programme (UNEP), Greening the Blue Helmets - Environment, Natural Resources and UN Peacekeeping Operations. UNEP: Nairobi, Kenya, May 2012.
UNEP, Assessment of Energy, Water and Waste Reduction Options for the Proposed AMISOM HQ Camp in Mogadishu, Somalia and the Support Base in Mombasa, Kenya. UNEP: 2010.

## Slide 13: Operational Energy Management Planning
Raise Awareness
  Train personnel on energy management requirements, behavior practices and responsibilities
  Coordinate with other functions as needed to ensure safe procedures and protocols
Implement plan and monitor performance of energy systems
  Implement corrective actions or reset energy usage goals
  Maintain documentation
Responsibility for energy use management and energy best management practices may evolve as the camp matures from initial to sustained operations
Energy
awareness
Energy conser-vation
Energy efficiency
2017_ver 1.0
Notes: Another important element of the plan is to raise awareness among all deployed personnel at the camp to help shape their behavior and familiarize them with standard operating procedures to reduce energy demand. Training for personnel directly involved with operation, maintenance and monitoring of equipment must be established and must include safety procedures and protocols.
The plan should be implemented and monitored to determine any areas of concern, opportunities for improvement, or any changes in mission. Documentation must be maintained; this is especially important because of changeovers in personnel.
Responsibility for energy use management and energy best management practices may evolve as the camp matures from initial to sustained operations.
Further reading/references: NATO AJEPP 2 /STANAG 2582 Best EP Practices for Military Camps, Annex F.

## Slide 14: Additional Planning Considerations
Duration of the mission affects the feasibility of renewable energy source options
  More mature camps may have higher energy demands to enhance quality of life
Host nation considerations:
  Energy use of the base camp should not exceed or strain the host nation infrastructure
  In areas with little or no energy resources, personnel should be conscious of the perception of excess energy usage
Photo credit: UNHCR
Photo credit: Swedish FOI
2017_ver 1.0
Notes: Expected mission duration will also affect the range of energy options applicable.
Energy consumption is strongly related to ambient conditions such as climate and camp population. As the population in a camp increases, so does the need for energy to fuel additional functions such as morale and welfare needs.
Lack of energy is a challenge in most developing countries and conflict regions. When using host nation power production infrastructure, it is important to consider how that use impacts the local community.
In cases where the camp is generating its own power, if the deployed forces are using significantly greater energy than the local community, it may generate a negative view of the force’s presence.
Upper Picture: Concept picture of a mature base camp.
Lower Picture: Solar power lamp used so that children are able to do their homework at night, in IDP/refugee camps

## Slide 15: Additional Planning Considerations
Feasibility of common renewable resources:
  Solar radiation
  Geothermal
  Sustainable wind speeds
  Biomass availability
100% Fossil fuels (e.g., diesel generators)
Fossil fuels as back-up and for peak production only
100% Renewable energy sources
Renewable energy as an addition
Balanced use of fossil fuels and renewables
Dependency on external fuel supply
High CO2-emissions
Self-sustainment in energy supply
Low CO2-emissions
Picture credits: http://solargis.info/
2017_ver 1.0
Notes: As camps mature, greater consideration may be given to the efficacy of using renewable resources to meet some energy requirements. These may include the types listed on the slide although this is not meant to be a comprehensive list.
Prior to any deployment, planners should refer to the deployment area’s irradiation mapping to determine the feasibility of using solar/PV power. See for example
http://solargis.info/ and http://solargis.info/doc/_pics/freemaps/1000px/ghi/SolarGIS-Solar-map-World-map-en.png
Planners must coordinate with the engineer and logistics staffs to determine the optimal combination of renewal energy resources and fossil-based energy resources to meet mission requirements. The timeline depicted on the slide illustrates the possible transition and benefits in moving toward more renewable energy sources in order to lower CO2 emissions and logistics requirements. These actions will enhance mission resiliency.

## Slide 16: Examples of Energy Reduction Practices
Use energy efficient equipment
    LED lightening
    Low-flow shower heads
    Microgrids for integrated power sources
Energy conservation
    Seal leaks
    Use natural lighting
    Shading
    Directional siting of structures
  Behavioral change
    Limited shower durations
    Turning off lights, computers
    Eliminating unnecessary idling of vehicles
    Economic driving, e.g. no fast starts or sudden stops
2017_ver 1.0
Notes: The slide lists a few examples of good energy practices.

## Slide 17: Related Energy Planning Aspects
Fuel Storage Capacity | Force Protection | Spill and Releases | Air Quality | Noise
Photo credits: Swedish FOI
2017_ver 1.0
Notes: Energy is an integral part of camp operations and is also closely related to several other areas, such as
POL storage
Force protection
Spill prevention and response
Air quality in the vicinity of generators (locally) and carbon footprint (regionally and globally)
Noise
By reducing the need for diesel fueled generators, all of the above-mentioned considerations are addressed.
Because of all the interdependencies present, it is important to take an integrated approach that considers all aspects.

## Slide 18: Uses and Examples
2017_ver 1.0

## Slide 19: General Use of Energy in Operations
Infrastructure & Equipment
  Lights, computers, alarms, medical, etc.
  Air heating and cooling
  Appliances (e.g., kitchen, laundry)
  Waste-water collection, treatment and disposal
  Solid waste collection, disposal/ incineration
Utilities
  Water extraction, treatment and distribution
  Water heating
  Refrigeration
Transportation
  Aviation
  Vehicles and ground equipment maintenance
2017_ver 1.0
Notes: Energy use in operational conditions is more difficult to predict than in the civilian society. This slide lists a range of typical energy uses in an operation.

## Slide 20: Examples of Energy Usage
General Example:
Command Post Exercise (CPX) ENERGEX, 2012 - NATO ENSEC COE (Lithuania)
Energy Demand Challenges:
  Camp Nobel, Mali - Swedish Armed Forces (SwAF)
Seasonal Variations in Energy Usage:
  Camp Northern Lights, Afghanistan – SwAF
Real-Time Energy Monitoring:
  Operation Nanook 2012, Inuvik, Canada – Canadian Armed Forces
2017_ver 1.0
Notes: This slide lists several examples of energy use during exercises and deployments. Each is addressed in more detail in the following slides.

## Slide 21: Example of Energy Consumption in Conventional Camp
End use | Size (Kwh) | Hours Run | Energy (Kwh) | Co2 (T) | Notes % from all energy
Lighting (external) | 208 | 1 825 | 999 546 | 249 | 6 %
Lighting (internal) | 61 | 7 300 | 1 168 000 | 292 | 7.5 %
Cooling | 333 | 7 300 | 6 387 500 | 1597 | 41 %
Hot Water | 180 | 3 650 | 1 815 395 | 454 | 11.5 %
Small Power (Accommodation) | 158 | 7 300 | 3 028 008 | 760 | 19.5 %
Small Power (Office) | 82 | 7 300 | 1 959 474 | 490 | 12.5 %
Catering | 16 | Various | 155 449 | 39 | 1 %
Ventilation (fans) | 0 | 0 | 0 | 0 | Assumed natural ventilation
Transport | NA | NA | NA | NA | Outside scope
Total | 1046 | 34 675 | 15 520 371 | 3 880 | 
Note: Facts from SWE CAMP Northern Lights MEZ AFGH 2013, 550 PAX
2017_ver 1.0

## Slide 22: CPX ENERGEX 2012 - NATO
Main Consumers of Fuel
Chart: 
| Power production | Heaters | Transportation | Incinerator | Other uses
Försäljning | 77.3 | 12 | 4.7 | 2.6 | 3.4
Activity | Fuel consumption liters (l) / month
Power production: Accommodation Offices HQ Kitchen, mess-hall Communication Recreation Others | (total 90 000) 36 000 11 700 8 100 7 600 4 500 4 500 17 600
Heaters | 14 000
Transportation | 5 500
Incinerator | 3 000
Other users | 3 900
Total | 116 400
2017_ver 1.0
Notes: This slide shows results from a NATO Command Post Exercise (CPX) ENERGEX 2012, designed to analyze how different constraints of energy supply could affect the sustainability of military capabilities in an operational environment. Exercise participants were encouraged to apply creative thinking and look for innovative solutions concerning energy supply-related issues.
The biggest consumer of energy (fuel) in winter time was main electricity generators. Main energy (fuel) users are written in decreasing consumption sequence
The main electricity generators ≈ 90 000 liters (l) of F35 per month = 77.3%
It was necessary to prevent water from freezing in storage. Heaters for Water tanks ≈ 14 000 l per month = 12%
Transportation assets (LTU) ≈ 5500 l per month = 4.7%
Incinerator (for waste incineration) ≈3 000 l per month = 2.6%
Other users (transportation assets, ESKO including contractor transportation, engineering assets) ≈ 3 900 l per month =
Total 116, 400 l
Main electricity generators provide electricity for:
Downlisted users (amount of fuel needed to produce electricity, l. per month.):
Accommodation (≈ 36 000 l.); = 40%, Offices (≈ 11 700 l.); = 13%, HQ (TOC) (≈ 8 100 l.); = 9 %, Kitchen, mess-hall (≈ 7 600 l.); = 8,4 %, Communication equipment (≈ 4 500 l.); = 5 %, Recreation: welfare building, sport hall, sauna (≈ 4 500 l.); = 5 %, Others (medical, sanitary, laundry, etc.) ≈17 600 l.) = 19,6 % = Total: 90 000 l
Reference/further reading
Drawn from COL Romualdas PETKEVIČIUS, Director NATO Energy Security Centre of Excellence, NATO Command Post Exercise (CPX) ENERGEX, 2012, The Sustainable Military Compounds (Towards a Zero Footprint Compound) (Chatham, United Kingdom, 8 – 11 October 2012).

## Slide 23: CPX ENERGEX 2012 - NATO
Offices, HQ & communication - 27 %
Accommodations - 40%
Other; medical, sanitary, laundry, workshops
etc. - 20 %
Welfare - 5 %
Kitchen & mess hall - 8 %
2017_ver 1.0
Notes: The numbers included in this slide are a rough estimation of energy consumption within the camp based on figures from the NATO Command Post Exercise (CPX) ENERGEX, 2012. (see previous slide)
These are NOT actual measured energy consumption at Camp Castor.
Furthermore, these numbers DO NOT include other energy uses as described in ENERGEX (see previous slide), that is Transportation assets, Incinerator (for waste incineration), Other users (transportation assets, ESKO including contractor transportation, engineering assets) or any Heaters for Water tanks (to prevent water freezing in storage).
Break down:
Accommodations = 40%
Recreation = welfare building, sport hall, sauna 5%
Kitchen and mess-hall = 8.4%
Administrative =
Offices (≈ 11 700 l.) = 13%
HQ (TOC) (≈ 8 100 l.) = 9%
Communication equipment (≈ 4 500 l.) = 5%
Other = medical, sanitary, laundry, etc. (3 900 l.) = 20%

## Slide 24: Camp Nobel, Mali - Swedish Armed Forces
Energy Demand Challenges
High consumption of diesel for operations
Periodic lack of fuel for operations due to high consumption and limited fuel supply
Poor fuel quality resulted in poor local air quality and equipment efficiency
Some older equipment required more fuel than newer equipment would have required
No alternative energy sources installed (per December 2015)
Picture credits: FOI (Swedish research agency)
Note:
SWE Camp Nobel Mali
(Timbuktu) 2014,
made for 250 Pax.
2017_ver 1.0
Notes:   Camp Nobel is a camp composed primarily of tents for living and operating space. It is a multi-national camp but the challenges listed above were those experienced by the Swedish Armed Forces (SwAF).
  Sufficient access to energy is a prerequisite for SwAF operations in Mali and elsewhere.
  The SwAF needs to increase its understanding of energy consumption and how to minimize the unnecessary waste of energy.
  In addition, the UN DPKO/DFS’ Environmental Policy for UN Field Missions (2009) , para 37 demands that: the mission “will take measures to ensure that the use of energy is optimized by the mission with the aim to minimize the mission’s greenhouse-gas emissions while ensuring enough power for proper functioning.”
  Reference/further reading:
  UN DPKO/DFS, Environmental Policy for UN Field Missions (2009), para 37

## Slide 25: Camp Northern Lights, Afghanistan, 2011-2012 Swedish Armed Forces
Seasonal variations for energy usage throughout one year in Afghanistan
During the 2011-2012, 25 air-conditioning units and kitchen facilities consumed 24% of all electrical energy at the camp (550 Pax) the entire year.
Week
2017_ver 1.0
Notes: In 2012, the Swedish Armed Forces assigned a student at the Royal Institute of Technology to assess the consumption of energy at Camp Northern Lights (CNL), Afghanistan.
The slide shows a breakdown of the electricity consumption during certain weeks in 2011 and 2012. On average, the consumption was approximately 34 000 liters per week (approximately 75% of a fuel truck).
The largest consumers were the kitchen facilities and the 25 air conditioning units, which alone accounted for 24.4% of the total consumption.
Reference/further reading
Johan Ihlis, Campers energi. Kartläggning och analys av energiförbrukningen i Camp Northern Lights. Kandidatexamensarbete KTH: Institutionen för hållbar utveckling. 2012.

## Slide 26: Real-Time Energy Monitoring Operation NANOOK 2012, Canada
Refrigeration
14%
2017_ver 1.0
Notes: The concept of sustainability was demonstrated through equipment and energy monitoring including: Vehicle Wash System, Mobile Incinerator, Reverse Osmosis Water Purification Unit (ROWPU), Mobile WastewaterTreatment Plant (WWTP), Variable Speed Generators.
  The data collected revealed a total camp consumption of 32,086 kWh for both diesel and propane for a week in August with an average camp population of 181 personnel (out of 320 possible).
The monitoring also showed that 85% of the total amount of diesel delivered to the camp was used by the generator farm to produce electricity and domestic hot water heating. A peak electrical demand of 247 kW and a total energy consumption of 22,279 kWh were recorded.
The largest electric load during the exercise went to provide space heating for soldier accommodations. This load represents 33% of the total electricity generated on site. The kitchen, food preparation and ablution as well as the refrigeration units took another 23%, while the Tactical Operations Centre and the offices required 19%. The vehicle fueling station, transport and Electric Mechanical Engineers (EME), vehicle washing station and Central Material Traffic Terminal (CMTT) required 12%. The remaining loads were for the Reverse Osmosis Water Purification Unit (ROWPU) and sewage, which accounted for 9%, and a single ablution which required 4%.
Reference/ further reading
L. Chubbs, “Canadian Case Studies on Energy Efficiency During Operations,” NATO EnvSec CoE Energy Security: Operational Highlights, No. 6, 2014.
Cassolato et al, “Operational Energy: A Multi-Faceted Government Approach,” NATO EnvSec CoE Energy Security: Operational Highlights, No. 7, 2014

## Slide 27: Production, Storage and Distribution
2017_ver 1.0

## Slide 28: Potential Energy Sources and Technologies
Sources:
Biomass
Biogas
Natural gas
Wind
Solar
Solid waste
Host-nation infrastructure
Photo credit: Canadian Forces
Photo credit: Swedish FOI
2017_ver 1.0
Technologies:
Generators
Photovoltaic Cells
Solar thermal
heating
Wind turbines
Micro-hydro
installations
Waste to energy
Micro grid
Hybrid systems
Notes: Currently, generators are the most common source of locally produced electricity in military operations. More broadly, trends favor renewable energy sources such as solar and wind power over non-renewables as they become more efficient and less expensive.
The description on some of the following slides also includes a rough ”Duration Suitability Index,” which indicates what is more feasible in the short, medium, and long term. It’s important to note, however, that these descriptions present only a conceptual comparison and the actual feasibility will vary from operation to operation and with geographical location and season. Case-by-case return on investment calculations and proof of concept will need to be performed.

## Slide 29: Energy Production Fuel-Powered Generators
Advantages
  Well-known, reliable concept
  Low upfront capital cost
Disadvantages
  High operating costs
  High maintenance requirements
  High logistics burden
  Ineffective
  Noisy
  Spill risks
Limitations
  Fuel availability
  Fuel quality
Duration Suitability Index |  | 
Short | Medium | Long
  Savings up to 30% - 50% possible due to demand-controlled power generation/ variable generators
Photo credit: Swedish FOI
2017_ver 1.0
Notes: Diesel generators are the most common way to support energy requirements at camps. Variable speed generators are better than standard generators because of their ability to manage the power output depending on power loads. Varying generator speed ensures more efficient fuel management that leads to fuel savings of 29% - 33%.
Generators seldom operate at their full capacity. In locations where no local grid is available, operations must be energy self-sufficient. Hence, generators are typically oversized to meet peak power demand plus a contingency factor. For example, the US Marine Corps sums the peak power demand of all known systems and chooses a generator that will support the summed load at 80%. If all equipment loads were constant, then the problem of right-sizing generators would not be challenging. However, it has been found that the load in the field varies daily, weekly and seasonally.
Although diesel generators are a reliable power source, the efficiency and reliability of generators decrease significantly when they are under-loaded. Generators running at low loads cause three major problems: 1) Poor fuel efficiency, 2) Increased maintenance, 3) Decreased lifespan of the system. One way to reduce this problem is to store energy, e.g. in batteries. The batteries increase the time the generators can be operated at peak power (peak performance). When the batteries are fully charged, the generators can be shut down and the batteries operate the systems until they are discharged to a certain level, at which point the generators reengage. This minimizes fuel consumption, prolongs the life time of the generators and decreases the need for generator maintenance.
Further reading/references:
B. Newell and E. B. Shields, USMC Expeditionary Energy Office Report on Expeditionary Energy Data Collection within Regional Command Southwest, Afghanistan. USMC Expeditionary Energy Office: September 2012.

## Slide 30: Energy Production Photovoltaic Cells/Solar Thermal
Advantages
  Low operating cost
  Low maintenance requirements
  Low logistical burden
  Several possible applications
Disadvantages
  High upfront capital cost
  Low energy production per unit area
  Vulnerable to attack
  Maximum benefit requires battery storage
Limitations
  Lack of sunlight (latitude, hill slope, orientation, shading, etc.)
  Requires secondary power source
Duration Suitability Index |  | 
Short | Medium | Long
Photo credits: EDA, FOI, and Franceski et al 2014
2017_ver 1.0
Notes: Falling prices for solar panels make solar power an increasingly attractive investment.
Solar power should not be used as the sole source of power, however, as it is intermittent and requires energy storage systems (batteries).
System performance degrades over time due to environmental effects on PV panels.
  Further reading/references:
  Annica Waleij, Daniel Westerlund, Birgitta Liljedahl, Experiences of Solar Energy Technologies during Field Conditions. FOI-R-4204-SE (Stockholm, Sweden: FOI, 2015).
  Franceski et al, “Off-grid Solar PV Power for Humanitarian Action: From Emergency Communications to Refugee Camp Micro-grids,” Procedia Engineering, Volume 78, 2014, pp. 229–235.
  “EDA installs energy management equipment at EUTM Mali camp,” https://eda.europa.eu/info-hub/press-centre/latest-news/2015/10/13/eda-installs-energy-management-equipment-at-eutm-mali-camp.

## Slide 31: OE Activities
Right-sized PV system + designed distribution system replaced spot generators
Significant fuel savings, increased reliability and power capability
Removed transportation challenges of moving fuel to a remote location
Enhanced operational capability by removing risk of power shortfall or system failure
Niamey
Replaced spot generators with properly sized and distributed system
Reduced total load
Improved redundant power capability
265K litres of fuel & 1.7€M in savings!
35KW Solar panel in Chad
Repurposed system from Afghanistan
Included automatic transfer switch for backup generator when sunlight is not adequate
“We are fuel independent at our base in Chad through Solar Power panels” – LTC Lockridge JAN 15 site report
Energy Production Photovoltaic Application in Africa
Source: USAFRICOM
2017_ver 1.0

## Slide 32: Energy Production Wind
Advantages
  Low operating cost
  Low logistics burden
Disadvantages
  High upfront capital cost
  May disturb mission-essential equipment (radar, aircraft)
  Vulnerable to attack
  Maximum benefit requires battery storage
  Noise
Limitations
  Access to sufficient wind
  Requires secondary power source
Duration Suitability Index |  | 
Short | Medium | Long
Photo credit: Canadian Forces
Picture credit: Swedish FOI
2017_ver 1.0
Notes:   Wind turbines may create localized background noise for radars or be vulnerable to attack and hence be unfavorable for military operations.
Despite the challenges, a wind power feasibility study at the EUFOR Butmir camp in Bosnia and Herzegovina found that with acceptable winds (10.2 m per second), a 30-40 percent proportion, combined photovoltaic-wind power generation solution could save 70% in energy costs compared to 100% diesel generation.
Possible adverse effects on local wildlife should also be considered.
The Canadian Forces also use wind power for short-term, section-sized deployments in the Arctic.
  Feasibility hence must be assessed on a case-by-case basis.
Further reading/references:
M. Righi, EUFOR feasibility study. Internal document. (Butmir, Sarajevo: EUFOR, 2008), p. 8.

## Slide 33
Wind
Diesel Generators
Waste to Energy
Solar
Energy Storage
System
Biogas
Energy Distribution
Hybrid Systems and Micro-Grids
2017_ver 1.0
Notes: Hybrid systems and micro-grids each make efficient use of the available power and reduce the need for peak power generation by managing the supply of power based on demand.
Renewable energy systems may be less reliable than more conventional systems and thus require secondary or additional power sources.
References/Further reading
R. Nazira, H. D. Laksonoa, E. P. Waldia, E. Ekaputrab, P. Coveriaa, “Renewable Energy Sources Optimization: A Micro-Grid Model Design,” Energy Procedia 52 (2014 ), pp. 316 – 327.
IEC (International Electrotechnical Commission), White Paper: Microgrids for Disaster Preparedness and Recovery with Electricity Continuity Plans and Systems, 2014.
Binayak Bhandari, Kyung-Tae Lee, Gil-Yong Lee, Young-Man Cho, and Sung-Hoon Ahn, “Optimization of Hybrid Renewable Energy Power Systems: A Review,” International Journal of Precision Engineering and Manufacturing – Green Technology, Vol. 2, No. 1 (Janurary2015 ), pp. 99-112 /99.

## Slide 34: Energy Efficiency
2017_ver 1.0

## Slide 35: Energy Efficiency A Holistic Approach in Practice
MAXIMUM ENERGY EFFICIENCY IS A
THREE-PRONGED APPROACH
  Behavioral change
  Energy efficient technologies
  Energy Conservation
2017_ver 1.0
Notes: At least three different perspectives need to be kept in mind for an holistic approach! Examples of each approach are listed on slide 16.

## Slide 36: Energy Efficiency Facilities
Facility planning and building zoning
  Natural shading, window coatings
Lighting (internal, external, natural lightning)
  LED or occupancy sensors
  Heat transfer technologies, heat pumps, hot water
  Air tightness, insulation, ventilation
  Variable speed electric motor drives
  Solar for thermal and electrical use, insulated hot water systems, water-efficient systems
Canadian Armed Forces (aka, ”Awesome Henry”)
2017_ver 1.0
Notes: When using LED lighting, it is often recommended to not use occupancy sensors. Occupancy sensors may draw more power than the LED lights.
Energy efficient light bulbs include halogen incandescent, compact fluorescent lamps (CFLs), and light emitting diodes (LEDs). Such lights typically use about 25%-80% less energy than traditional bulbs and last 3-25 times longer. LED lighting is preferred over the other types due to lower energy requirements, smaller size, greater longevity, and fewer disposal concerns.
Heat transfer technologies include using excess heating or cooling for space climate control, water, etc.
References/Further reading
US Department of Energy, Energy Saver. Tips on Saving Money & Energy at Home, 2009.
UNDP, Guidelines for Energy Savings, 2015.
U.S. Energy Information Administration, AEO2014 Early Release Overview.
http://energy.gov/sites/prod/files/2014/09/f18/61628_BK_EERE-EnergySavers_w150.pdf

## Slide 37
UNINSULATED INTERIORS
Common spaces
Assembly areas
Equipment storage / dressing rooms
Passages connecting the zones
COVERED EXTERIORS
Parts of the accommodation areas
Storages
EXTERIORS
Recreational facilities in accommodation areas
INSULATED INTERIORS
Sleeping quarters
Office spaces
Briefing / meeting rooms
Sanitary facilities
Drying rooms
Common spaces in harsh environments
Saunas
Energy Efficiency
Zoning by Use
2017_ver 1.0
Notes: “The properties of a space should match the function conducted in a space. For example, the sleeping quarters need to be cool enough for sleeping but equipment doesn't necessarily need to be stored in air conditioned space. To achieve this, spaces are divided into different zones. The spaces where people spend most of their time, sleeping or working, are to be insulated and cooled. However, the spaces that are visited only temporarily can be uninsulated. Common spaces, assembly areas, storages and passages are suitable to be placed in uninsulated space.”
“The goal is to optimize the share of insulated interior space. By doing this, construction and transport costs can be lowered, construction time shortened and energy consumption reduced.”
Reference
Turkka Ehramaa, ”Sustainability of Semi-Permanent Buildings in International Operations.” Master’s thesis in architecture.

## Slide 38
Energy Efficiency
Passive Cooling Methods
2017_ver 1.0
Notes: A building’s orientation has a significant effect on passive cooling and heating. The sun typically shines from a lower angle from the east and west than it does from the south, so larger overhangs are required for shading on the east and west sides of buildings than on the south side.
Reference
Turkka Ehramaa, ”Sustainability of Semi-Permanent Buildings in International Operations.” Master’s thesis in architecture.

## Slide 39: Energy Efficiency Air Sealing
Thorough air sealing substantially increases the energy efficiency of structures
Air infiltrates in and out through every hole and crack
About 30% of air leaks through openings in ceilings, walls and floors
2017_ver 1.0
Notes: Warm air leaking in during the summer (and in warm climates) and leaking out during the winter (and in cold climates) can waste a lot of energy.
Reference/Further reading
U.S. Energy Information Administration, AEO2014 Early Release Overview, http://energy.gov/sites/prod/files/2014/09/f18/61628_BK_EERE-EnergySavers_w150.pdf
US Department of Energy, Energy Saver. Tips on Saving Money & Energy at Home, 2009, http://www.cees.ingersollrand.com/CEES_Documents/Energy_Saver_Tips.pdf

## Slide 40: Energy Efficiency Efficient Use of Heaters and Air Conditioners
Use centrally regulated systems and programmable thermostats
Keep doors and windows closed to prevent loss of conditioned air
Perform preventative maintenance on schedule
Reduce heating and air conditioning in spaces that are only used for short periods
Shut down heating and air conditioning systems when not required
2017_ver 1.0
Notes: Heating and air conditioning consume a significant portion of energy in the camp. Efficient use of heaters and air conditioners saves a significant amount of energy.

## Slide 41: Energy Efficiency Use and Behavior
Skilled operation and maintenance staff for power production and distribution
Efficient use of motorized equipment (reduce or eliminate unnecessary idling)
Metering of main consumption points and centralized monitoring of energy use
2017_ver 1.0
Notes: Maintenance is very important to ensure optimal performance and energy efficiency of equipment.
Ensure that only qualified technicians or trained personnel perform maintenance.
Metering, while not necessary, is ideal for understanding overall camp energy consumption and where efficiencies in the system can be made.

## Slide 42: Energy Efficiency Conservation Actions
Use power management settings on computers and turn off lights when not needed
Eliminate unnecessary vehicle use
Ensure dishwashing and laundry machines are full before being operated
Take shorter showers
Use natural lightning when possible
Turn off the tap when brushing teeth or shaving
Photo credit: Swedish FOI
Conserving resources conserves energy!
2017_ver 1.0
Notes: In order to accelerate and streamline the processes of enabling and embedding energy efficiency in operations, it is necessary to change human behavior in a number of ways. Cultural changes, if properly designed and applied, can facilitate energy efficiency as a low-cost way of addressing energy security, environmental and economic challenges. It has been demonstrated that behavioral change can contribute to energy efficiency and improved environmental performance with multiple positive consequences.
Brief personnel on the basics of energy use, such as turning off lights when not in use, closing doors, or water conservation. It is ideal to brief personnel before the deployment. During the deployment, consider posting information signs to remind personnel about energy efficiency actions.
Remember: resource conservation is ALSO energy conservation. It takes energy to move resources to where you are!
References/Further Reading
NATO EnSecCoE Advanced Research Workshops on Enhancing Energy Efficiency in NATO through Behavior Change.
42

## Slide 43: Conclusion and Key-Take Aways
Energy efficiency is a tactical issue for the commander and planning staff
Energy conservation saves money and lives
Environmental and energy issues need to be integrated early in the planning process
There’s no ”right answer”…each situation requires its own solution
2017_ver 1.0
Notes: The operational capability and capacity of the camp will be greatly affected by the planning and final implementation of the energy production and distribution systems.

## Slide 44: References
2017_ver 1.0

## Slide 45: Energy in NATO Environmental Policy / Doctrine
Document | Source | Energy mentions
Policy | MC469/1 (14 Oct. ‘11) - NATO Military Principles and Policies for Environmental Protection (EP) | No mention
Doctrine | AJEPP 4/ STANAG 7141 Joint NATO EP Doctrine during NATO-led Military Activities | Multiple mentions …Ensure careful use of energy sources/ supplies… …energy efficiency/conservation awareness/responsibilities…
Procedures/ Instructions | AJEPP 5 /STANAG 2510 Joint NATO Waste Management | No mention
 | AJEPP 6/STANAG 6500 NATO Compound Environmental File | No mention
 | AJEPP 1 /STANAG 2581 EP Standards and Norms for Military Camps | Annex F. Energy
 | AJEPP 2 /STANAG 2582 Best EP Practices for Military Camps | Annex F - Infrastructure Planning and Energy Conservation
 | AJEPP 5 /STANAG 2583 EMS in NATO Operations | Multiple mentions ..Sources of energy … energy efficiency …
 | AJEPP 7 /STANAG 2594 Best EP Practices for Military Training Areas | Multiple mentions …energy dissipation… energy depletion… energy intense…
2017_ver 1.0
Notes: Energy issues in particular, are also covered by several of NATOs EP documents (i.e. policy, doctrine, procedures and instructions), shown on this slide

## Slide 46: Other NATO Energy Activities
NATO Energy Security Center of Excellence (ENSEC COE), Lithuania
NATO Smart Energy Team
NATO Library Guide on Energy Security
http://www.natolibguides.info/smartenergy
2017_ver 1.0
Notes: The ENSEC COE is located in Vilnius, Lithuania. Its aim is to provide qualified and appropriate expert advice on questions related to operational energy security. Among other things, it arranges Advanced Research Workshops (ARWs) and an Energy Security Strategic Awareness Course. The first course was held in the fall of 2015.
A special Science for Peace and Security funded activity was the “Smart Energy Team” (SENT), comprised of experts from Allied and partner countries. In 2013 - 2015, national and NATO documents were screened and various defence agencies were visited to identify practical energy efficient solutions.
A Smart Energy Library Guide has been created and is maintained by NATO’s Emerging Security Challenges Division (ESCD).
Further reading/references:
NATOs Energy Security Center of Excellence (ENSEC COE) http://www.enseccoe.org/en/home.html
Energy Security Strategic Awareness Course http://www.enseccoe.org/en/news/the-first-energy-sw1c.html
NATO Smart Energy Team (SENT) final report http://www.natolibguides.info/ld.php?content_id=18110194
NATO Library Guide on Energy Security http://www.natolibguides.info/energysecurity

## Slide 47
Energy conservation
Amounts and type of energy required for the camp sites
Investigation of possible use of renewable energy sources
UN climate neutrality
Changing behavior!
Recommended Actions:
Install wind-driven ventilators
Install visible thermometers & hygrometers to monitor temperature & humidity
Choose energy-efficient appliances & lighting
Use renewable energy devices for water heating and electrical appliances where affordable/practical
Promote Eco driving
The mission “will take measures to ensure that the use of energy is optimized by the mission with the aim to minimize the mission’s greenhouse-gas emissions while ensuring enough power for proper functioning.”
UN DPKO/DFS Environmental Policy for UN Field Missions (2009), para 37
UN Peacekeeping and Energy
2017_ver 1.0
Notes: Energy conservation and efficiency is a part of the UN DPKO/DFS’ Environmental Policy for UN Field Missions (June 2009).
In order to reduce the environmental and carbon footprint of UN peacekeeping, several mission are investing in renewable energy sources, and solar thermal heaters are available through UN systems contracts.
Further reading/references:
UN DPKO/DFS, Environmental Policy for UN Field Missions (2009), para 37.
UNEP, Assessment of Energy, Water and Waste Reduction Options for the Proposed AMISOM HQ Camp in Mogadishu, Somalia and the Support Base in Mombasa (2010).
United Nations Environmental Programme (UNEP), Greening the Blue Helmets - Environment, Natural Resources and UN Peacekeeping Operations (Nairobi, Kenya: UNEP, May 2012).
B. Liljedahl, M. Rydbo, E. Martinsson, and A. Waleij, Energy Efficient UN-camp - Repayment on Additional Investment. FOI-SH--0078—SE (Umeå, Sweden: Swedish Defence Research Agency (FOI), 2009).

## Slide 48: References
European Union (EU)
  The 2012 Energy Efficiency Directive (http://ec.europa.eu/energy/en/topics/energy-efficiency/energy-efficiency-directive) establishes a set of binding measures to help the EU reach its 20% energy efficiency target by 2020. Under the Directive, all EU countries are required to use energy more efficiently at all stages of the energy chain from its production to its final consumption.
  Additional sources of information about EU guidance and assessments include:
  European Defence Agency (EDA). “Military Green 2013 Climate, Environmental and Energy Security – From Strategy to Action Report from Workshop Series 6 – 7 June and 13 June 2013.” See https://www.eda.europa.eu/what-we-do/activities/activities-search/european-armed-forces-go-green
  “EDA installs energy management equipment at EUTM Mali camp,” https://eda.europa.eu/info-hub/press-centre/latest-news/2015/10/13/eda-installs-energy-management-equipment-at-eutm-mali-camp
European External Action Service (EEAS). European Union Military Concept on Environmental Protection and Energy Efficiency for EU-led military operations. EEAS (14 September 2012)
Righi, M. EUFOR Feasibility Study. Internal document. EUFOR: Butmir, Sarajevo, 2008, p. 8
North Atlantic Treaty Organization (NATO)
NATO’s Energy Security Center of Excellence (ENSEC COE), http://www.enseccoe.org/en/home.html
NATO’s Library Guide on Energy Security, http://www.natolibguides.info/energysecurity
NATO’s Energy Security Strategic Awareness Course, http://www.enseccoe.org/en/news/the-first-energy-sw1c.html
NATO’s Smart Energy Team (SENT) final report, http://www.natolibguides.info/ld.php?content_id=18110194 (2015)

## Slide 49: References
NATO (continued)
NATO Wales Summit Declaration, http://www.nato.int/cps/ic/natohq/official_texts_112964.htm (September 2014)
NATO Chicago Summit Declaration, http://www.nato.int/cps/en/natohq/official_texts_87593.htm?selectedLocale=en (May 2012)
NATO Military Principles and Policies for Environmental Protection (EP), MC469/1 (14 October 2011)
NATO Strategic Concept of 2010. ”Active Engagement, Modern Defence” (para 15), http://www.nato.int/cps/en/natohq/topics_82705.htm
United Nations (UN)
United Nations Development Programme (UNDP). Guidelines for Energy Savings (2015)
United Nations Environmental Programme (UNEP). Greening the Blue Helmets - Environment, Natural Resources and UN Peacekeeping Operations. Nairobi, Kenya: UNEP, May 2012
”On the Establishment of MINUSMA.” S/RES/2100 (April 2013) http://www.un.org/en/peacekeeping/missions/minusma/documents/mali%20_2100_E_.pdf
UNEP. Assessment of Energy, Water and Waste Reduction Options for the Proposed AMISOM HQ Camp in Mogadishu, Somalia and the Support Base in Mombasa (2010)
UN DPKO/DFS. Environmental Policy for UN Field Missions (2009)
Moving Towards a Climate Neutral UN: The UN System’s Footprint and Efforts to Reduce It (2009 edition) http://www.greeningtheblue.org/sites/default/files/MovingTowardsAClimateNeutral%20UN.pdf

## Slide 50: References
Sweden
Liljedahl, B., M. Rydbo, E. Martinsson, and A. Waleij. Energy Efficient UN-Camp - Repayment on Additional Investment. FOI-SH—0078-SE. Umeå, Sweden: Swedish Defence Research Agency (FOI), 2009
  Waleij, Annica, Daniel Westerlund, and Birgitta Liljedahl. Experiences of Solar Energy Technologies during Field Conditions. FOI-R-4204-SE. Stockholm, Sweden: FOI, 2015
Waleij, A. and J. Hedström. ”A Life Cycle Perspective on Camps- Complex Issues Handled Holistically.” FOI MEMO 4935 (2014)
Waleij, A., K.D. Mattson, J. Berggren, J. Hedström, and B. Liljedahl. “Holistic Camp Planning to Address the Cumulative Environmental Footprint from Military and Civilian Actors Operating in the Same Area.” Proceedings from the European Conference of Defence and the Environment 2013. Helsinki: 2013-05-20 - 2013-05-21, s.23-28
  Waleij, A., M. Östensson, D. Harriman, and C. Edlund. Greening Peace Operations - Policy and Practice. FOI-R--3112—SE. Stockholm, Sweden: FOI, 2011
United States
Newell B. and E. B. Shields. USMC Expeditionary Energy Office Report on Expeditionary Energy Data Collection within Regional Command Southwest, Afghanistan. USMC Expeditionary Energy Office: September 2012
U.S. Department of Energy. Energy Saver. Tips on Saving Money & Energy at Home. Washington, DC: DOE, 2009.
U.S. Energy Information Administration, AEO2014 Early Release Overview. http://energy.gov/sites/prod/files/2014/09/f18/61628_BK_EERE-EnergySavers_w150.pdf

## Slide 51: References
Other
  Bhandari, Binayak, Kyung-Tae Lee, Gil-Yong Lee, Young-Man Cho, and Sung-Hoon Ahn. “Optimization of Hybrid Renewable Energy Power Systems: A Review.” International Journal of Precision Engineering and Manufacturing – Green Technology, Vol. 2, No. 1 (January 2015), pp. 99-112 at p. 99
  Cassolato et al. ”Operational Energy: A Multi-Faceted Government Approach.” NATO EnvSec CoE Energy Security: Operational Highlights, No. 6 (2014)
  Franceski et al. “Off-grid Solar PV Power for Humanitarian Action: From Emergency Communications to Refugee Camp Micro-grids,” Procedia Engineering, Volume 78 (2014), pp. 229–235
Green Defence Framework, http://static.sdu.dk/mediafiles//C/2/0/%7BC20727DA-FDA3-4002-BB25-BE49FC1C2F47%7DLloyd%20Chubbs%20AC281-N(2013)0096-REV4%20of%202014_01_23%20GREEN%20DEFENCE.pdf
International Electrotechnical Commission (IEC). White Paper: Microgrids for Disaster Preparedness and Recovery with Electricity Continuity Plans and Systems (2014)
Irradiation mapping can be found, for example, at http://solargis.info/ or http://solargis.info/doc/_pics/freemaps/1000px/ghi/SolarGIS-Solar-map-World-map-en.png
Nazira, R., H.D. Laksonoa, E.P. Waldia, E. Ekaputrab, and P Coveriaa. “Renewable Energy Sources Optimization: A Micro-Grid Model Design,” Energy Procedia 52 (2014), pp. 316 – 327